## Slide 1: TAS – Autonomous Driving and parking roboter
TAS - Final Presentation/Report
Prof. Dr. Wollherr, Khoi Hoang Dinh
Christopher Zeiser, David Full, Hans Böhme

## Slide 2: Table of Contents
Motivation
Task 1
  Map Saving
  Parameter Optimization
  Single-Goal Autonomous Driving
Task 2
  Simulation Extension
  Flexible Parking
Summary

## Slide 3: Motivation
Interesting facts about autonomous driving:
2025 - Law and insurances are ready
2035 - 20-35% autonomous cars
Accident reduction by 15% thanks to car assistant systems in the past 10 years in Europe

## Slide 4: Task 1 – Map Saving
Record map with hector mapping
 ‘run1.launch‘
2. Save map with „map_saver“ service
 ‘run2.launch‘ and ‘run2.sh‘
3. Start necessary nodes
 ‘run3.launch‘
 Flexible starting position

## Slide 5: Task 1 - Parameter Optimization
Preset parameters for each car
Forward and backward speed
Steering angle offset
Parameter server for real time driving optimization
Additional speed (forward and backward)
Additional steering angle offset
Local/Global planner parameters
Notes: Inflation radius, Obstacle avoidance factor, Obstacle look ahead factor, Tolerances, Maximum velocity, Cost map parameters

## Slide 6: Task 1 – Single-Goal Autonomous Driving
  Reducing the number of waypoints to one
  Independent of map shape and size, only low requirements close to the robot
  Possible to start at nearly every position
   High flexibility

## Slide 7: Task 1 – Single-Goal Autonomous Driving
Idea:
Change the map temporarily by faked laser data.
Approach:
Wait until wall is published
Set goal directly behind the car
Start autonomous driving
Remove the wall and slightly correct the goal to the starting position

## Slide 8: Task 1 – Single-Goal Autonomous Driving
U-shaped wall behind the car
Relevant area in green

## Slide 9: Task 2 - Simulation Extension
Additional parking slot
Additional slalom course
8 different starting positions accessable on simulation startup
roslaunch tas_simulator startSimulation.launch pos‘x‘:=1

## Slide 10: Task 2 – Flexible Parking
New parking node for laser (position) + imu (orientation) communication.
Task implemented with final state maschine like approach
Start park procedure with pressing the A-button
Detect parking slot and drive to starting position
5 binary coded state indicators + 7 states + formulas depending on car indicators, states and parking attempt (left – right, in - out)

## Slide 11: Task 2 – Flexible Parking
current_orientation == start_orientation
current_roentation == start_orientation 45°
car in parking slot
car near the wall in the parking slot
front_scan == back_scan
 Truth tables for velocity and steering angle
LSB
MSB

## Slide 12: Summary
Stable autonomous driving + obstacle avoidance
Parking with flexible side and (un-)parking and partially independence of starting position
Optimized simulation
Optimized parameters for all treated application
Problems and feedback
Hardware issues (LAN, bluetooth, screen)
Software issues (malfunctioning simulation)
Car issues (battery, steering parameters)

## Slide 13: Thank you for your attention!